## Slide 1: Biomechanics
7ο εξάμηνο
Σχολή Μηχανολόγων Μηχανικών ΕΜΠ
Διδάσκων:
Michael Neidlin
Fritz Kahn (1888 – 1968)
FE Analysis&Course Grading
Information

## Slide 2: Course guideline
Do the simulations with your model or use this
https://www.dropbox.com/s/j4jg6knwaizlir2/femur.stl?dl=0
The simulation process is the following (Help is provided on the next slides):
1. Read in the stl model and load into Static Structural
2. Define surface thickness (if necessary of e.g. 4 mm)
3. Mesh the model. Automatic method, shell mesh should be produced
4. Create Named selections for fixed b.c., Femur neck and Joint loading location (simplest case is Nodal Force at one node). Create boundary conditions
5. Create hyperelastic material through material fitting
6. Run the simulation for one case. See if it works out. Result evaluation through User Defined Results
7. Do Mesh Independence then do your study!
8. Sum up study in a report

## Slide 3: Report and Course Evaluation
After the FEA study please submit a short written report (about 2-5 pages) on methods, results and discussion.
You can do this in groups of 2-5 people if you wish.
There is no need in being exhaustive, however I am especially interested to see some critical thoughts on the short project that you did.
What can we generally get out of the results?
What were the limitations? What would you improve if you had a lot of time? How do you think these kind of analyses could help. And so on, be creative.
The deadline is 16.01.2018.
Please do the survey below to evaluate the course (max. 5 min):
https://www.surveymonkey.com/r/QQS55P8